# ARP and RARP
LESSON 7

## (September 27, 1995)
Daniel Z. Tabor Jr.
New Jersey Institute of Technology

## Outline:
ARP and RARP

| The Address Resolution Problem Physical Addresses: Mapping Address Resolution Protocol (ARP) ARP Inefficiencies and Improvements ARP Functionality | ARP Header Fields Booting with Physical Addresses Reverse Address Resolution Protocol (RARP) Primary and Backup RARP Servers RARP Header Fields |
| --- | --- |

## The Address Resolution Problem:

- ? How does a host or gateway map an IP address to the correct physical address when it needs to send a packet over a physical network ?

- Devise a low-level software that hides physical addresses and allows higher-level programs to work only with internet addresses.

- Mapping of high-level to low-level addresses is the address resolution problem.

| IP address A | conceptual | B IP address |
| --- | --- | --- |
| Physical address A | physical | B Physical address |

## Physical Addresses:

- Two basic types of physical addresses:

  - Large

    - Ethernet

    - 48 bits

  - Small

    - Token Ring (proNET-10)

    - 8 bits

- proNET-10 - uses Class C addresses with host-id portion = 1, 2, ... , 255

## Physical Addresses:
Mapping

- Mapping must be computationally efficient (simply mask all portions of the address excluding the host-id portion)

- When address mapping can only be done via an address table (X.25 to IP), hashing is used to speed up lookup.

- Problem with representation of 48-bit Ethernet addresses within a 32-bit IP address and allowing new machines to be added without recompilation.

- Avoid maintaining a static table of mappings by using the ARP (Address Resolution Protocol).

## Address Resolution Protocol (ARP):

- ARP - is a low-level protocol used to bind addresses dynamically.

- ARP allows a host to find a physical address of a target host on the same physical network, given only it’s IP address.

- ARP hides the underlying network physical addressing. It can be thought of as part of physical network system and not the internet protocols.

- ARP broadcasts special packets with the destination’s IP address to ALL hosts.

- The destination host (only) will respond with it’s physical address.

- When the response is received, the sender uses the physical address of destination host to send all packets.

## ARP Inefficiencies and Improvements:

- Broadcasting is expensive on network resources, so an ARP cache of recently acquired IP-to-Physical address bindings is kept.

- Other Broadcast Improvements:

  - Include the sender’s IP-to-Physical address binding along with the request, to the destination. This reduces future traffic.

  - During each broadcast, ALL machines can find out the senders physical address and record it locally in it’s ARP cache.

  - When a new machine comes on-line, it immediately broadcasts it’s IP-to-Physical address binding to all nodes.

## ARP Functionality:

- There are two main functional parts of the address resolution protocol:

  - Determine the destination’s physical address before sending a packet.

  - Answer requests that arrive for it’s own Physical-to-IP address binding.

- Because of lost/duplicate packets, ARP must handle this to avoid many re-broadcasts.

- Bindings in ARP cache (actual cache table) must be removed after a fixed period of time to ensure validity.

- When a packet is received, the sender’s IP address is stripped and the local table is updated (ARP cache), then the rest of the packet is processed.

- Two types of incoming packets:

  - Those to be processed (correct destination).

  - Stray broadcast packets (can be dropped after updating the ARP cache).

- Application programs may request the destination address many times before the binding is complete. This must be handled, by discarding enqueued requests, when the correct binding returns.

- ARP sets the field "TYPE" for the ID of a frame.

- ARP packets DO NOT have a fixed format header, so they can be used with arbitrary physical addresses and arbitrary protocol addresses.

- The lengths of physical addresses may vary up to 48-bits.

## ARP Header Fields:

- Hardware Type: (16-bits) - the type of interface the sender seeks an answer for.

- Protocol Type: (16-bits) - the high-level software address type provided.

- HLEN: (8-bits) - length of arbitrary physical address.

- PLEN: (8-bits) - length of arbitrary protocol address.

- OPERATION: (16-bits) - the specific type of operation requested.

  - ARP.request (1)

  - ARP.response (2)

- SENDER HA: (6-octets) - the sender’s actual hardware address, scalable up to six bytes.

- SENDER IP: (4-octets) - the sender’s IP address, always 32-bits.

- TARGET HA: (6-octets) - the destination node’s hardware address, scalable up to six bytes.

- TARGET IP: (4-octets) - the destination node’s IP address, always 32-bits.

## Booting with Physical Addresses:

- Machines without secondary-storage (diskless workstations) that cannot store their IP addresses need to find out by broadcasting their physical address and requesting a binding to the appropriate IP address.

- Terminals and nodes cannot connect to their fileservers without using source and destination IP addresses.

- IP addresses should not be bound into a machines bootstrap image. Not doing so allows for flexibility and convenient changes to configuration information.

- A connection is needed at start-up to allow the diskless workstation to begin functioning (sends request to a server and waits for the response).

- To provide the connection, workstations include a minimal set of TCP/IP protocols in firmware.

- Two advantages of using a unique physical address:

  - Physical address is available from the network interface hardware and does not have to be bound into the operating system.

  - The machine ID depends on the network (not it’s CPU) so all machines will be given uniform and unique IDs.

## Reverse Address Resolution Protocol (RARP):

- RARP functionality supports multiple physical network types.

- All machines receive RARP requests but only those authorized to supply RARP services can respond. Machines supplying RARP services are called RARP servers.

- RARP is only used on LANs with a low probability of failure since bootstrapping requires quick responses.

## Primary and Backup RARP Servers:

- Primary servers respond while backup servers simply record the time of the incoming requests.

- If the primary server is down, backup server will see reoccurring requests and take over. This take over is done by using a random delay to see if other backup servers respond first.

## RARP Header Fields:

- RARP requests and responses use the same frame format as ARP, however the OPERATION field value differs.

- OPERATION: (16-bits) - the specific type of operation requested.

  - RARP.request (3)

  - RARP.response (4)

Top of Form